Abstract Dataplane
29-04-2015

---
P4 language
- Programming Protocol-Independent Packet Processors
- High-level
- More flexible as OpenFlow
- http://p4.org/

---
P4 model
Queues
and/or
Buffers
Match
+ Action
Match
+ Action
Ingress Match + Action
Packet Modifications +
Egress selection
Egress Match + Action
Packet Modifications
INPUT
OUTPUT
PARSER

---
P4 source (match +action)
control ingress {
    apply(table1);
    apply(table2);
}
control egress {
    apply(table3);
    apply(table4);
}
Sequential execution
Sequential execution

---
P4 source (match +action)
control ... {
    if cond {...}
    else {...}
    ...
    apply (...) {
      apply_match {
        ...
      }
    }
}
Control can be
more difficult...
Control based on
table matching
or the applied function

---
P4 source (match + action)
table table_name {
    reads {
        metadata.field : exact;
        header.field : lpm;
    }
    actions {
        action1;
        action2;
    }
    size : TABLE_SIZE;
}
Matching type
(exact, terbary, lpm,
range, valid)
Fields used by matching

---
P4 source (match + action)
table table_name {
    reads {
        metadata.field : exact;
        header.field : lpm;
    }
    actions {
        action1;
        action2;
    }
    size : TABLE_SIZE;
}
Allowed action functions

---
P4 source (match + action)
Simultaneous execution
(according to the
specification)
action fname(params) {
    primitive_action1(params1);
    primitive_action2(params2);
}
Primitive actions
(from an extensible set)

---
Currently available
- Compiler frontend
- Behavioral compiler backend
        (created by Barefoot Networks, Inc.)
Some example for the compiler
        (created by Barefoot Networks, Inc.)

---
Current solution
P4 source
Abstract
Syntax
Tree
compiler
frontend
Template files
(hardvare dependent
description)
backend
based on
 a template engine
 (tenjin)
C source

---
Template files
Python script
(using the AST)
//:: for x in list_calc():
int function_${x}(params) {
  ...
  //:: ...
 }
C like code as text
fast prototype
very hard to maintain
no validation (e.g. typecheck)