## Slide 1: data plane use cases
For comparable measurement results with OpenFlow (OVS, ERFS), P4 and other SDN/NFV pipelines (BESS, VPP)

## Slide 2: use case summary
Hardware related test cases
  NIC delay + bandwidth
Simple use cases
  l2fwd + l3fwd
  data center gateway (vxlan)
Complex core network use cases
  simplified mobile gateway (GTP, rate policing, l2fwd, l3fwd only)
  complex mobile gateway
  BNG
Radio base station (only packet processing unit)
  PDCP + TN
  PDCP + TN + RLC + Air scheduler
End-to-end use cases
  service chaining

## Slide 3: hardware related test cases

## Slide 4: nic delay
Test setup
  2 back-to-back connected servers
Measurement
  Read tsc
  DPDK packet TX
  Host 2 forwards back the packet
  DPDK packet RX
  Read tsc
  Calculate RTT
TODO: use NIC rules @ host2
Host 1
DPDK app
Host 2
NIC
DPDK l2fwd
NIC
TX tsc
RX tsc
  Some results (Xeon E5-1650 v2 @ 3.50GHz)
  Intel X540-AT2 10Gbit (RJ45)
    Min/Med/99.9 - 11.5/11.6/21 us
  Intel LX710 40Gbit (QSFP+ copper)
    Min/Med/99.9 - 6.7/6.9/16.5 us
  Mellanox MT27700 40Gbit (QSPF+ copper)
    Min/Med/99.9 - 2.3/2.4/11 us

## Slide 5: nic bw
Test setup
  2 back-to-back connected servers
  Allocate as many cores to both pktgen and l2fwd as possible
  Measurement
    DPDK packet TX
    Host 2 forwards back the packet
    DPDK packet RX
    Calculate bandwidth
      small (64B) pkts: max pps
      large (1500B) pkts: max bps
  TODO: use NIC rules @ host2
Host 1
DPDK pktgen
Host 2
NIC
DPDK l2fwd
NIC
TX tsc
RX tsc

## Slide 6: simple use cases
L2, L3 forwarding, DC Gateway

## Slide 7: l2 forward
Configuration
  before test
  use trace to populate tables
    SMAC  MAC learn
    DMAC  MAC fwd
Tests:
  uni/bi-directional
  1-2-4-8-… cores
  64-1500 byte packets
In: physical 10/40/100G
Out: physical 10/40/100G
L2 learn + forward with different table sizes
  1+1 rule
  10k+10k S/DMAC rules
  100k+100k S/DMAC rules
Traces:
  1 packet per DMAC rule
  packet sizes:
    64, 128, 256, 512, 1024, 1280, 1500
  random SrcIP and DstIP (for RSS to work)
  filenames:
    nfpa_trL2_1_random.<pktsize>.pcap
    nfpa_trPR_<nrules>.<pktsize>.pcap
out port
MAC fwd
key: DMAC
type: Hash
entries: 1/10k/500k
MAC learn
key: SMAC
type: Hash
entries: 1/10k/500k

## Slide 8: l3 forward
Configuration
  before test
  use trace
  set S/DMAC
  routes should match traffic
Tests:
  uni/bi-directional
  1-2-4-8-… cores
  64-1500 byte packets
In: physical 10/40/100G
Out: physical 10/40/100G
L2 + ARP + L3 with different routing table sizes:
  10k prefixes (edge router)
  400k prefixes (hbone)
Traces:
  1-10-100-1k-10k-100k random IP flows
  no black hole route for these DstIPs
  packet sizes:
    64, 128, 256, 512, 1024, 1280, 1500
  filenames:
    nfpa_trL3_<nrules>_random_hbone.<pktsize>.pcap
out port
Layer 3 part
Layer 2 part
own MAC && type = IP
option 1
option 2

## Slide 9: l3 fwd pipeline option #1 (openflow-based)
ARP select
key: Ethertype
entries: 2
type = 0x0800 (IP)
L3 (FIB)
key: (VLAN,) IP.dst
type: LPM
entries: (50 x )10k / 400k
Nexthop Groups
type = indirect
bucket Actions:
set-field SMAC
set-field DMAC
decrease TTL
Output (port)
type = 0x0806 (ARP)
own MAC + broadcast
normal L2 fwd
no match
ARP to router IP answer: Own MAC
CP (Ryu)
MAC learn
key: SMAC
type: Hash
entries: nexthops
no match
MAC fwd
key: DMAC
type: Hash
entries: nhops + ports
out port
Notes: © Ericsson AB 2015
9

## Slide 10: l3 fwd option #2: separated l2 and l3
Ethertype key: Ethertype
entries: 2
type = 0x0800 (IP)
L3 (FIB)
key: IP.dst
type: LPM
entries: 10k / 400k action: save nexthop (e.g. to metadata)
ARP table
key: nexthop (metadata)
type: Hash
entries: nexthops
action: set DMAC
type = 0x0806 (ARP)
own MAC + broadcast
normal L2 fwd
no match
ARP to router IP answer: Own MAC
MAC learn
MAC learn
key: SMAC
type: Hash
entries: nexthops
no match
MAC fwd
key: DMAC
type: Hash
entries: nhops + ports
action: set SMAC, send
physical port
ARP
RIB
L2 pipeline
L3
Notes: © Ericsson AB 2015
10

## Slide 11: l3 forward with VRF
Configuration
  before test
  use trace
  set S/DMAC
  routes should match traffic
Tests:
  uni/bi-directional
  1-2-4-8-… cores
  64-1500 byte packets
In: physical 10/40/100G
Out: physical 10/40/100G
Same as L3 fwd, but with VLAN based VRF support
  50 x 10k routes
Traces:
  same as for the previous, but with VLANs
  1-10-100-1k-10k-100k random IP flows
  no black hole route for these DstIPs
  packet sizes:
    64, 128, 256, 512, 1024, 1280, 1500
  filenames:
    nfpa_trL3_<nrules>_random_hbone.<pktsize>.pcap
out port
Layer 3 part
Layer 2 part
own MAC && type = IP
option 1
option 2

## Slide 12: l3 fwd with vrf support high-level overview
MAC learn
(Common) L2 part
S/DMAC lookup
VLAN lookup
ARP VRF #1
external port
VRF #2 L3 fwd
prefix -> nexthop lookup
nexthop -> DMAC lookup
set DMAC
send back to L2 fwd
VRF #1 L3 fwd
prefix -> nexthop lookup
nexthop -> DMAC lookup
set DMAC
send back to L2 fwd
internal port VRF #1
internal port VRF #2
RIB VRF #1
…
ARP VRF #2
RIB VRF #2
…
…
virtual ports and logically separated VRFs are only needed in case of OpenFlow where number of tables are limited – in other cases L2 part could select the proper VRF L3 fwd tables directly
Notes: © Ericsson AB 2015
12

## Slide 13: l3 fwd with vrf support
Ethertype key: Ethertype
entries: 2
type = 0x0800 (IP)
L3 (FIB) #i
key: IP.dst
type: LPM
entries: 10k action: save nexthop (e.g. to metadata)
ARP table #i
key: nexthop (metadata)
type: Hash
entries: nexthops
action: set DMAC
type = 0x0806 (ARP)
own MAC + broadcast
normal L2 fwd
no match
ARP to router IP answer: Own MAC
MAC learn
MAC learn
key: SMAC
type: Hash
entries: nexthops
no match
MAC fwd
key: DMAC
type: Hash
entries: nhops + ports
physical port
ARP
RIB
VRF select
key: VLAN
entries: 50
virtual port #i
L2 pipeline
L3
Notes: © Ericsson AB 2015
13

## Slide 14: DC gateway vxlan + load balancing + l3/l2
Configuration
  before test
  use traces + next slide
  set S/DMAC
  routes should match traffic
Tests:
  2 x uni + bi-directional
  1-2-4-8-… cores
  64-1280 byte packets
In: physical 10/40/100G
Out: physical 10/40/100G
Data Center Gateway, different UL/DL
  UL (incoming): IP packets to different services
    load balance to internal addresses
      based on SrcIP (sender’s IP)
      use 100 different virtual services (= DstIP)
    use VxLAN tunneling
  DL (outgoing): VxLAN encapsulated packets
    remove VxLAN tunnel + do L3 and L2 fwd
Traces:
  Uplink: 10k IP packets, 100 different DstIP, random SrcIP, DMAC = GW
  Downlink: 10k VxLAN packets
    external: DstIP = GW, 200 different SrcIP (blade), DMAC = GW
    internal: SrcIP = service, 10k different DstIP
  packet sizes:
    64, 128, 256, 512, 1024, 1280
  filenames:
    TBD
out port
Layer 3 part
Layer 2 part
Layer 4 part (LB)

## Slide 15: dcgw pipeline
Load Balancer
LB key: SrcIP
Actions:
push VxLAN
set external IP addresses
(set DMAC?)
Load Balancer
LB key: SrcIP
Actions:
push VxLAN
set external IP addresses
(set DMAC?)
ARP select
key: Ethertype
entries: 2
L3 (FIB)
key: (VLAN,) IP.dst
type: LPM
entries: 10k
Nexthop Groups
type = indirect
bucket Actions:
set-field SMAC
set-field DMAC
decrease TTL
Output (port)
type = 0x0806 (ARP)
own MAC + broadcast
normal L2 fwd
no match
ARP to GW IP or service VIP answer: Own MAC
CP (Ryu)
MAC learn
key: SMAC
type: Hash
entries: nexthops
no match
MAC fwd
key: DMAC
type: Hash
entries: nhops + ports
out port
LB selector
key: IP.dst
type: hash
entries: 100 + 1
Load Balancer
LB key: SrcIP
Actions:
push VxLAN
set external IP addresses
(set DMAC?)
VxLAN pkt (egress)
(pop VxLAN)
dst = GW_IP
default
dst = service VIP
Notes: © Ericsson AB 2015
15

## Slide 16: complex core network test cases

## Slide 17: simplified mobile gw gtp, rate limit, l2/l3
Configuration
  before test
  use traces + next slide
  set S/DMAC
  set IP addresses + TEIDs
    use same TEIDs UL/DL
  do not do fragmentation (limit MTU)
  routes should match traffic
Tests:
  2 x uni + bi-directional
  1-2-4-8-… cores
  64-1280 byte packets
    to avoid fragmentation
    (if needed we can test it later)
In: physical 10/40/100G
Out: physical 10/40/100G
Mobile Gateway, different UL/DL
  UL (from UE): GTP encapsulated packets
    L2, L3 and L4 check (GW, UDP, 2152)
    GTP decaps, save TEID
    rate limit per bearer (TEID)
    L3 routing towards Internet + L2 fwd
  DL (to UE): normal IP packets
    L2 and L3 check (DstIP is in UE range)
    DstIP -> rate limit + GTP encaps + set ext DstIP
    L3 routing towards BSTs + L2 fwd
Traces:
  Uplink: 10k GTP packets from 100 Base Stations (BSTs)
    external: DstIP = GW, DMAC = GW, SrcIP = BST(i)
    internal: DstIP = server (1k), SrcIP = UE (10k)
  Downlink: 10k IP packets, SrcIP = server, DstIP = UE
  packet sizes:
    64, 128, 256, 512, 1024, 1280
  filenames:
    TBD

## Slide 18: mobile gw pipeline simplified: only GTP + rate limit
Rate limiter #1
Rate limiter #1
Ethertype
key: Ethertype
entries: 2
L3 fwd block
(see L3 fwd case)
type = 0x0806 (ARP)
own MAC + broadcast
ARP to GW IP answer: Own MAC
Infra CP
L2 fwd block
(see L2 fwd case)
IP + UDP select
key: IP.dst, UDP dport
entries: 2
GTP handler
(pop GTP, save TEID)
UL: GW IP, UDP, 2152
DL: DstIP in UE range
Rate limiter #i
key: TEID
UE selector
key: IP.dst
type: Hash
entries: 10k
actions: push GTP, set IP
out port
Notes: © Ericsson AB 2015
18

## Slide 19: virtual mobile gw infra, gtp, rate limit, firewall, etc.
Configuration
  roughly same as previous
  set IP addresses + TEIDs
    use same TEIDs UL/DL
  do not do fragmentation (limit MTU)
  firewall rules should match servers
    UL: check destinations
    DL: check sources
  routes should match traffic
Tests: same as previous
  2 x uni + bi-directional
  1-2-4-8-… cores
  64-1280 byte packets
    to avoid fragmentation
    (if needed we can test it later)
In: physical 10/40/100G
Out: physical 10/40/100G
DL (to UE):VxLAN encapsulated normal IP packets
  L2 and L3 check (physical MAC and IP, type VxLAN)
  VxLAN decapsulation
  L2 check
  L3 check (DstIP in UE rng)
  global firewall rules
  bearer select (TFT, DstIP)
    optimal lookup?
  rate limit per bearer - or ECM flagging
  volume accounting + event generation
  GTP encapsulation (TEID, DstIP, SrcIP)
  traffic management
  L3 routing towards S1U
  VxLAN encapsulation
  L3 routing towards DCGW
  L2 fwd
UL (from UE): VxLAN encapsulated GTP packets
  L2 and L3 check (physical MAC and IP, type VxLAN)
  VxLAN decapsulation
  L2, L3 and L4 check (GW, UDP, 2152)
  GTP decapsulation
  global firewall rules
  bearer select (TEID)
  rate limit per bearer - or ECM flagging
  volume accounting + event generation
  traffic management - e.g. Priority queuing + WFQ between same prio users/bearers
  L3 routing towards Gi
  VxLAN encapsulation
  L3 routing towards DCGW
  L2 fwd
infra

## Slide 20: virtual mobile gw full pipeline (including infra)
APP
INFRA
Ethertype
key: Ethertype
entries: 2
L3 block
(internal)
type = ARP
own MAC broadcast
Infra CP
L2 block
(see L2 fwd case)
IP + UDP select
key: IP.dst, UDP dport
entries: 2
GTP handler
(pop GTP, save TEID)
UL: GW IP, UDP, 2152
DL: DstIP in UE range
Rate limiter #1
Rate limiter #1
Rate limiter #i
key: TEID
UE selector
key: IP.dst
type: ternary or hierarchical
entries: 10k
actions: push GTP, set IP
out port
VxLAN (VxLAN -> pop VxLAN)
Firewall UL
key: L3, L4
entries: 100
action: drop
Rate limiter #1
Rate limiter #1
Counter #i
key: TEID
Traffic Mgmt block
VxLAN
(push VxLAN)
type = IP
L3 block
(external)
Firewall DL
key: L3, L4
entries: 100
action: drop
Notes: © Ericsson AB 2015
20

## Slide 21: Broadband nw gw (BNG) gRE, rate limit, traffic mgmt, nat, L2/L3
Traces:
  Uplink: 10k GRE packets
    external:
      DstIP = BNG
    internal:
      DstIP = servers (1k)
      SrcIP = UE (10k)
  Downlink: 10k IP packets
    SrcIP = servers
    DstIP = NAT address
    ports: according to NAT
  packet sizes:
    64, 128, 256, 512, 1024, 1280
  filenames:
    TBD
DL (to users) trace:
  normal IP
Pipeline:
  L2 and L3 check (dst: BNG)
  NAT downlink
  generic firewall
  User select (DstIP)
    rate limit (police)
    GRE encaps
  traffic mgmt, WFQ between users (ID)
  L3 routing towards users + L2 fwd
UL (from users) trace:
  GRE encapsulated IP
Pipeline:
  L2, L3 and type check (dst: BNG, type: GRE)
  GRE decaps, save ID
  rate limit per user (ID)
  generic firewall
  NAT uplink
  traffic mgmt, WFQ between users (ID)
  L3 routing towards Internet + L2 fwd

## Slide 22: BNG
Ethertype
key: Ethertype
entries: 2
type = ARP
own MAC broadcast
Infra CP
L2 block
(see L2 fwd case)
IP + type select
(IP.dst, IP.type)
GRE handler
(pop GRE, save ID)
UL: DstIP = BNG, type = GRE
DL: DstIP = NAT
Rate limiter #1
Rate limiter #1
Rate limiter #i
key: ID
UE selector
key: IP.dst
type: Hash
entries: 10k
actions: push GRE, set IP
out port
Firewall UL
key: L3, L4
entries: 100
action: drop
Traffic Mgmt block
type = IP
L3 block
(external)
Firewall DL
key: L3, L4
entries: 100
action: drop
NAT uplink
key: IP.src
NAT downlink
key: port
Notes: © Ericsson AB 2015
22

## Slide 23: radio base station test cases
Only PPU

## Slide 24: pdcp pipeline simple bst: gtp (s1U), pdcp, air crypto
Traces:
  UL: 10k X2 pkts from 100 Antennas
    external:
      DstIP = BST
      DMAC = BST
      SrcIP = Antenna(i)
    internal: Snow3G
      DstIP = server (1k)
      SrcIP = UE (10k)
  DL: 10k GTP pkts
    external:
      DstIP = BST, DMAC = BST
      SrcIP = MGW
    internal:
      SrcIP = server, DstIP = UE
  packet sizes: 64, 128, 256, 512, 1024, 1280
  filenames: TBD
DL (to UE) trace:
  S1U packets (GTP encapsulated normal IP)
  (possibly in IPSec tunnel)
Pipeline:
  (IPSec decrypt)
  L2, L3 and L4 check (BST, UDP, 2152)
  GTP decapsulation
  select UE (DstIP)
  Snow3G encryption
  GTP encapsulation
    TEIDin  TEIDout
    SrcIP = BST
    DstIP = Antenna
  L3 routing towards antenna site + L2 fwd
UL (from UE) trace:
  X2 packets (GTP encapsulated Snow3G)
Pipeline:
  L2, L3 and L4 check (BST, UDP, 2152)
  GTP decapsulation
  decrypt Snow3G
  select UE (SrcIP)  GTP encapsulation
    TEIDin  TEIDout
    SrcIP = BST
    DstIP = MGW
  (IPSec encryption)
  L3 routing towards Mobile GW + L2 fwd

## Slide 25: pdcp pipeline simplified BST
Ethertype
key: Ethertype
entries: 2
L3 fwd block
(see L3 fwd case)
type = 0x0806 (ARP)
own MAC + broadcast
ARP to GW IP answer: Own MAC
Infra CP
L2 fwd block
(see L2 fwd case)
IP + UDP select
key: IP.dst, UDP dport
entries: 2
GTP handler
(pop GTP, save TEID)
BST IP, UDP, 2152
out port
Snow3G decrypt
encrypted (UL)
unencrypted (DL)
UE select (UL)
key: TEID
entries: 10k (Hash)
actions: Push GTP, set IP
Snow3G encrypt
UE select (DL)
key: TEID
entries: 10k (Hash)
actions: Push GTP, set IP
Notes: © Ericsson AB 2015
25

## Slide 26: bst pipeline s1U, pdcp, crypto, scheduler, rlc
Traces:
  UL: 10k RLC pkts from 100 Antennas
    RLC framing
    DMAC = BST
    SMAC = Antenna
  DL: 10k GTP pkts
    external:
      DstIP = BST
      DMAC = BST
      SrcIP = MGW
    internal:
      SrcIP = server
      DstIP = UE
  packet sizes: 64, 128, 256, 512, 1024, 1280
  filenames: TBD
DL (to UE) trace:
  S1U packets (GTP encapsulated normal IP)
  in IPSec tunnel
Pipeline #1:
  IPSec decrypt
  L2, L3 and L4 check (BST, UDP, 2152)
  GTP decapsulation
  select UE (DstIP)
  Snow3G encryption
  RLC framing
  RLC buffering
  air scheduler
  L2 fwd
UL (from UE) trace:
  Antenna-specific frames (Ethernet, RLC)
Pipeline:
  L2
  RLC decode
  (reassembly)
  if RLC ACK: release RLC buf and finish processing
  send RLC ACK (in acknowledged mode)
  decrypt Snow3G
  select UE (SrcIP)  GTP encapsulation
    TEIDin  TEIDout
    SrcIP = BST
    DstIP = MGW
  IPSec encryption
  L3 routing towards Mobile GW + L2 fwd

## Slide 27: BST pipeline simplified BST
Ethertype
key: Ethertype
entries: 2
L3 fwd block
(see L3 fwd case)
type = 0x0806 (ARP)
own MAC + broadcast
ARP to GW IP answer: Own MAC
Infra CP
L2 fwd block
(see L2 fwd case)
IP + UDP select
key: IP.dst, UDP dport
entries: 2
GTP handler
(pop GTP, save TEID)
BST IP, UDP, 2152
out port
Snow3G decrypt
encrypted (UL)
unencrypted (DL)
UE select (UL)
key: TEID
entries: 10k (Hash)
actions: Push GTP, set IP
Snow3G encrypt
UE select (DL)
key: TEID
entries: 10k (Hash)
actions: Push GTP, set IP
todo…
Notes: © Ericsson AB 2015
27